MesosphEO WP 4.2:

MIPAS-IMK/IAA L2 Data ReadMe

M. Kiefer & S. Lossow, KIT

FMI-TN-MesosphEO-WP4-003

Version 1.0

10.4.2017

- Introduction	2

- Level2 screening	2

- Data gridding and units	3

- User guidance	3

- NetCDF format for MIPAS L2 data 	3

- References	6

- Introduction

This document explains the netCDF format used for MIPAS-IMK/IAA L2 data of several trace gases (CH4, CO, CO2, H2O, N2O, NO, NO2, Ozone, temperature) in the ESA’s MesosphEO project. The files conatin a month’s L2 data each and are named as follows:

MIPAS-E_IMK.<YYYYMM>.<citation_version>.nc

Here <YYYYMM> gives the year/month coded in 6 digits like, e.g., 200904 for April of 2009.

<citation_version> is a string which gives a unique identification of 1) the L1b data version used for the L2 data processing, 2) the retrieval target (gas, temperature) contained in the data file, and 3) the retrieval setup for the target. An example would be V5R_H2O_522: here V5R means that L1b comes from the measurement period of reduces spectral resolution and L1b data was processed by ESA with the IPF5.X software. The delivery within the MesosphEO project only contains V5R data. H2O denotes the target gas, which in this case is water vapour. If this middle entry is composed of two targets connected by a lowercase “w”, like in TwNO and NOwT, the target contained in the file is the former of the two.

The setup number 522 shows that the data was processed for the middle atmosphere mode (leading 5) with the setup specific to this gas of version number 522. Besides the 5XX setup numbers there are also 6XX and 7XX setup numbers. They denote processing of upper atmosphere and NLC mode data, respectively.

Examples:

MIPAS-E_IMK.201109.V5R_H2O_622.nc: All September 2011 water vapour data processed from reduced resolution upper atmosphere measurements using retrieval setup 622.

MIPAS-E_IMK.201204.V5R_NOwT_622: All April 2012 NO data processed from reduced resolution upper atmosphere measurements using retrieval setup 622 for the joint retrieval of  NO and temperature, not to be mixed up with NO data from the file

MIPAS-E_IMK.201204.V5R_NO_622 which contains data of „pure“ NO retrieval (height range of the two NO data products is different).

- Level2 screening

The data given in the files cover an altitude range which usually is greater than the valididty range of the data. Therefore the user should do some data screening:

The level2 screening differs for the different parameters, depending upon if they are based on a linear-space or a log-space retrieval.

For the CH4, CO2, N2O, Ozone and temperature data, which are retrieved in linear-space, the screening looks as follows:

- data points with a visibility flag of 0 are discarded

- data points with an average kernel diagonal element (aka AKD criterion) of less than 0.03 are discarded

- data above the uppermost tangent height are not considered any further.

For the CO, H2O, NO and NO2 data, which are retrieved in log-space, only screening (1) and (3) are applied.

- Data gridding and units

The data are provided on a fixed altitude grid. There is one gas/temperature profile per MIPAS measurement geolocation.

Temperatures are provided in K. The trace gases are given in volume mixing ratio, which is the basic unit. A detailed description of all data fields is given in Sect. 6.

- User guidance

The three MIPAS measurement modes do have the following altitude coverage:

middle atmospher (MA) 15 – 100 km

upper atmosphere (UA)  40 – 170 km

NLC mode (NLC)          40 – 100 km

However, in  the L2 processing only a subset of these altitude ranges is covered, namely:

MA (5XX) 15 – 100 km

UA  (6XX) 40 – 100 km (exception: NowT and TwNO: 40 – 170 km)

NLC (7XX) 40 – 100 km

Note that additionally the screening criteria as presented in Section 2 have to be applied.

- NetCDF format for MIPAS L2 data

The netCDF data files contain dimensional information, data variables, and global attributes. In detail there are:

Dimensions:

| No | Dimension name | Content |
| --- | --- | --- |
| 1 | timegrid | Number of measurements/geolocations |
| 2 | altgrid | Number of retrieval (result) altitude grid points |
| 3 | scangrid | Number of measurement altitude grid points |
| 4 | stringlength | Maximum stringlength |

Data:

| No | Variable | Unit | Dim | Description |
| --- | --- | --- | --- | --- |
| 1 | time | days | timegrid | Days since 1.1.1970, 00:00:00 |
| 2 | sub_id | n/a | timegrid x stringlength | IMK/IAA internal identifier |
| 3 | geo_id | n/a | timegrid x stringlength | geolocation identifier: 5 digits orbit number, 1 underscore, 16 digits date/time in ISO format |
| 4 | latitude | degrees north | timegrid | latitude, -90 to 90 deg |
| 5 | longitude | degrees east | timegrid | longitude, -180 to 180 deg |
| 6 | sza | degree | timegrid | solar zenith angle, 0 to 180 deg |
| 7 | dof | n/a | timegrid | degrees of freedom for retrieval result profile |
| 8 | chi2 | n/a | timegrid | Chi square for the retrieval |
| 9 | rms | n/a | timegrid | rms of the residual |
| 10 | eta | km | scangrid x timegrid | engineering tangent altitudes delivered with L1b data |
| 11 | eta_indices | n/a | scangrid x timegrid | indices of eta values used for the retrieval (e.g. clouds invalidate lower altitudes) |
| 12 | los | km | scangrid x timegrid | line of sight of tangent altitude from retrieval |
| 13 | visibility | n/a | altgrid x timegrid | flag to indicate whether this altitude contributes to measurement |
| 14 | altitude | km | altgrid x timegrid | altitudes of the retrieval grid, result data is given for this altitudes |
| 15 | target | K (for temperature) ppmv (for gases) | altgrid x timegrid | retrieval result, either temperature or gas |
| 16 | pressure | hPa | altgrid x timegrid | pressure at altitude |
| 17 | temperature | K | altgrid x timegrid | If target is temperature: this gives the apriori temperature If target is gas: this gives the temperature as retrieved from L1b data |
| 18 | target_noise_error | ppmv | altgrid x timegrid | estimated standard deviation of the retrieval result derived from spectral noise |
| 19 | akm_diagonal | n/a | altgrid x timegrid | diagonal entries of the averaging kernel matrix |
| 20 | vr_col | km | altgrid x timegrid | Vertical resolution as calculated from the columns of the averaging kernel matrix |
| 21 | vr_row | km | altgrid x timegrid | Vertical resolution as calculated from the rows of the averaging kernel matrix |
| 22 | vr_akdiag | km | altgrid x timegrid | Vertical resolution as calculated from the diagonal entries of the averaging kernel matrix |

The NetCDF files contain a number of global attributes. Of these only the following ones are important for the data user:

| No | attribute | meaning |
| --- | --- | --- |
| 3 | retrieval_in_logarithmic_parameter_space | Either TRUE (retrieval was done in logarithmic parameter space) or FALSE (linear parameter space); important for the application of the averaging kernel diagonal criterion (see Section 2) |
| 4 | use_data_only_in_altitude_range | Maximum altitude range the data can be used in; further restrictions apply, see Section 2 and next attribute entry: comment |
| 5 | comment | Explanation what should be used for data screening, see also Section 2 |

- References

ESA MesosphEO project plan, version 1.5, 2016